Broptics FBG Optic Sensor Specification

Model: Broptics OS1500

Date: 5/22/02

|  | DESCRIPTION | SPEC |
| --- | --- | --- |
| 1 | Center wavelength position | C-band (1530 ~ 1570nm) |
| 2 | Center wavelength tolerance@25℃ | < +/-0.1 nm |
| 3 | Reflective bandwidth @-0.5dB | 0.1 ~ 0.2 nm |
| 4 | Reflective bandwidth @-3dB | < 0.3 nm |
| 5 | Reflectivity | > 90% |
| 6 | Splicing loss per node | < 0.1dB |
| 7 | Side lobe suppression | > 20dB |
| 8 | Cladding mode loss (*) | < 0.2dB |
| 9 | Typical strain sensitivity | 1.20 pm/strain |
| 10 | Strain response linearity | < +/- 0.05 pm |
| 11 | Max strain by stretch | 2,000 strain |
| 12 | Max strain by compress | 8,000 strain |
| 13 | Typical temperature sensitivity | 11 pm/℃ |
| 14 | Temperature response linearity | < +/- 0.5 pm |
| 15 | Operation temperature range | -10℃ ~ 100℃ |
| 16 | Packaging type | Athermal packaged (<1pm/℃) Acrylate recoating (**) Bare FBG |
| 17 | Fiber in use | SMF-28 Single mode fiber |
| 18 | Pigtail length | cm to km |

(*) Lower cladding mode loss is available by using photo sensitivity special fiber

(**) Polyimide recoating will be available in late 2002